## Slide 1: Chapter 2 OSI Model & TCP/IP Protocol Suite
The OSI/RM
Layers in the OSI/RM
TCP/IP protocol suite
Addressing in TCP/IP
TCP/IP versions

## Slide 2: 2.1 The OSI/RM
An ISO standard
  Open System Interconnection/ Reference Model
  开放系统互连/参考模型
  Released in 1984
  Ensured greater compatibility and interoperability
  7 layers, each of which illustrates a particular network function
ISO is the organization, OSI is the model
OSI is not a protocol, but a conceptual model

## Slide 3: OSI Model
7
6
5
4
3
2
1
应用层
表示层
会话层
传输层
网络层
数据链路层
物理层
网络支持层
（软/硬件）
应用支持层
（软件）
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 4: Why Layered？
Advantages
  Reduces complexity
  Standardizes interfaces
  Facilitates modular engineering
  Ensures interoperable technology
  Accelerates evolution
  Simplifies teaching and learning
Disadvantages
  Strict layered architecture makes its software not so efficient.
…
N+1
N
N-1
…

## Slide 5: The Features of Layering
Each layer concerns on its own details
Each layer provides a service to the layer above
Each layer communicates with its peer layer in another node through the use of a corresponding protocol

## Slide 6: Peer-to-Peer Communication
对等进程/对等实体
（Peer Entity）
Peer Entity
对等进程/对等实体
对等层
Peer Layer
Peer Layer
对等层
Interface
接口
对等层协议
Peer-to-Peer Protocol
Peer-to-Peer Protocol
对等层协议
Service
服务

## Slide 7: Peer Layer vs. Peer Entity
Multiple entities in one layer
  Peer entity：存在通信关系的对等层实体
Multiple protocols in one layer
  Protocol：对等实体间的通信规则
CutFTP
FTP Server
Outlook
Mail Server
IE
WWW Server
Layer 7
Layer 7
Outlook
IE
CutFTP
FTP Server
Mail Server
WWW Server
FTP
HTTP
SMTP

## Slide 8: Data Exchange: Encapsulation
Source
Destination
A
P
S
T
N
DL
Ph
PDU：Protocol Data Unit
协议数据单元
帧 Frame
分组 Packet
数据段 Segment
数据 Data

## Slide 9: Postal Delivery
信件
邮局
分拣邮包
邮政网络
邮政运输
交通运输
信件
邮局
分拣邮包
邮政网络
邮政运输
信件格式
寄信方式
分拣邮包规则
邮路选择
运输方式
同层间需要约定规则——协议

## Slide 10: 2.2 Layers in the OSI/RM
Application
Presentation
Session
Transport
Network
Data Link
Physical
7
6
5
4
3
2
1
Network processes to applications
Data representation
Inter-host communication
End-to-end connections
Addressing and best path
Access to media
Binary transmission

## Slide 11: Physical Layer

## Slide 12: Date Link Layer

## Slide 13: Point-to-Point Delivery

## Slide 14: Network Layer

## Slide 15: Host-to-Host Delivery

## Slide 16: Transport Layer

## Slide 17: Reliable End-to-End Delivery of a Message

## Slide 18: Session Layer

## Slide 19: Presentation Layer

## Slide 20: Application Layer

## Slide 21: 2.3 TCP/IP Protocol Suite
OSI/RM
TCP/IP
The historical and technical open standard of the Internet
Wanted a network that could survive any conditions, even a nuclear war
Application
Presentation
Session
Transport
Network
Data Link
Physical
1
2
3
4
5
6
7
Application
Transport
Internet
Network
Access

## Slide 22: TCP/IP协议
Socket
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
LANs
MANs
WANs
DNS
TFTP
SNMP
ICMP
IGMP
ARP
RARP

## Slide 23: Multiplexing of TCP/IP Protocols
Telnet
FTP
SMTP
SNMP
TFTP
TCP
UDP
ICMP
IP
ARP
Ethernet
software
Ethernet
hardware
Port
Protocol ID
Type
MAC
23
21
25
161
69
6
17
1
0800H
0806H

## Slide 24: 2.4 Addressing in TCP/IP
Address
Physical address
物理地址
IP address
IP地址
Port address
端口地址
标识通信节点
节点所属LAN或WAN指定
LAN或WAN内唯一
链路地址/硬件地址
0x0005.5D06.1418
标识通信节点的网络连接
Internet指定
Internet内唯一
网络地址
202.115.12.34
标识通信进程
操作系统指定
一台计算机内唯一
21, 23, 25, 80
8080, 10000

## Slide 25: Relation-ship of Layers and Addresses in TCP/IP
Physical address
IP address
Port address
IP and other protocols
Network layer
Underlying physical networks
Network Access layer
Process
Application layer
TCP
UDP
Transport layer

## Slide 26: Example 1

## Slide 27: Example 2

## Slide 28: 2.5 TCP/IP Versions
Version 4（current）
  Insufficient address space: 32-bit
  Inefficient mechanism: poor QoS and security
Version 5
  A proposal on the OSI model
  Never went beyond the proposal stage
Version 6（future）
  Only change network layer protocols: IPv6, ICMPv6
  Large address space：128-bit
  Improve the weakness of version 4

## Slide 29: 2.6 Summary
对分层网络协议体系的理解
  不同节点：层次组成不同，作用不同
  横向理解：虚通信，对等实体，协议，PDU
  纵向理解：封装与解封，服务，接口
OSI/RM
  作用
  各层的名称和功能（概要描述）
TCP/IP
  层次：与OSI模型的对应关系
  协议：主要协议及其所在层次

## Slide 30: Summary（cont.）
Addressing
  物理、IP、端口地址：作用，所在层次
区别
  OSI vs. ISO
  Physical address vs. MAC address
  Network address vs. IP address