## Slide 1: Chapter 6 ARP and RARP
ARP
ARP package
RARP
Notes: 对应教材第4版的第8章

## Slide 2: Addresses
Host identifier
  IP address
  Physical address
Network
Data Link
Physical
Map

## Slide 3: Issues
A送往E的分组需封装在Ethernet帧中传送
  IP地址：全局性
  物理地址：本地性
A
A仅知道：IPA，MACA，IPE
Ethernet Frame：
IP Packet
？
E
B
C
D
目的MAC
类型
FCS
源MAC
MACA

## Slide 4: Address Mapping（地址映射）
Logical address  Physical address
Static mapping
Dynamic mapping
Static Table | 
Logical address | Physical address
…… | ……
…… | ……
Consider:
NIC changed
Mobile computer
Cache Table | 
Logical address | Physical address
…… | ……
…… | ……
Look for the target on demanding, using dynamic address resolution protocol

## Slide 5: ARP and RARP
ARP
Logical address
Physical address
RARP
Logical address
Physical address
Notes: 动态映射的协议有2个，ARP和RARP

## Slide 6: 6.1 ARP
Address Resolution Protocol，RFC 826
  地址解析协议：IP address  MAC address
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access
Layer
Transport Layer
Application Layer

## Slide 7: 6.1.1 ARP Operation
A: 1.2.3.1
E: 1.2.3.5
I’m looking for the physical address of a node whose IP address is: 1.2.3.5
I am the node you are looking for, and my physical address is: 0005.5D06.1418
Request
Request
Request
Reply
Request
Broadcast
Unicast
B: 1.2.3.2
C: 1.2.3.3
D: 1.2.3.4
IP address | MAC address
A’s ARP Cache：
1.2.3.5
0005.5D06.1418
bind

## Slide 8: 用户输入命令“ftp 主机名”时的操作
FTP
TCP
IP
ARP
以太网
驱动程序
主机名
解析器
以太网
驱动程序
以太网
驱动程序
IP地址
主机名
（1）
（2）
（3）
（4）
ARP
ARP
FTP
TCP
IP
（5）
（6）
（7）
目的

## Slide 9: IP Packet and ARP Packet
IP
IP
IP
IP
ARP request
ARP reply
IP packet
Binding B
IP packet
IP packet
IP packet
No binding
A
B
Binding A

## Slide 10: ARP Process Cases
Case 1：A  B
  In same IP network
  Lab 2
Case 2：A  D
  In different IP network
A
C
B
D
R1
R2
IPA，MACA
IPB，MACB
IPC，MACC
IPD，MACD
IP1
MAC1
IP2
MAC2
IP3
MAC3
IP4
MAC4

## Slide 11: Case 1：A  B
A
C
B
D
R1
R2
IPA，MACA
IPB，MACB
IPC，MACC
IPD，MACD
IP1
MAC1
IP2
MAC2
IP3
MAC3
IP4
MAC4
IP Address | MAC Address
A’s ARP Cache：
IPB
MACB
B’s ARP Cache：
IPA
MACA
R1’s ARP Cache：
sIP=IPA，dIP=IPB
ARP
request
ARP
request
ARP
request
ARP
request
ARP
reply
IP
IP
sMAC=MACA，dMAC=MACB
sIP=IPA，dIP=IPB
dMAC=广播，Target_IP=IPB

## Slide 12: Case 2：A  D
A
C
B
D
R1
R2
IPA，MACA
IPB，MACB
IPC，MACC
IPD，MACD
IP1
MAC1
IP2
MAC2
IP3
MAC3
IP4
MAC4
IP Address | MAC Address
A’s ARP Cache：
IP1
MAC1
B’s ARP Cache：
R1’s ARP Cache：
IPA
MACA
sIP=IPA，dIP=IPD
ARP
request
ARP
request
ARP
request
ARP
request
ARP
reply
IP
IP
sMAC=MACA，dMAC=MAC1
sIP=IPA，dIP=IPD
dMAC=广播，Target_IP=IP1
IPD不在本网内，分组由R1转发
sMAC=MAC2，dMAC=MAC3
sIP=IPA，dIP=IPD
sMAC=MAC4，dMAC=MACD
sIP=IPA，dIP=IPD
IP1是A的缺省网关（Default Gateway）

## Slide 13: 6.1.2 ARP Packet
Hardware Type |  | Protocol Type
Hardware address len | Protocol address len | Operation Request 1, Reply 2
Sender hardware address （For example，6 bytes for Ethernet） |  | 
Sender protocol address （For example，4 bytes for IP） |  | 
Target hardware address （For example，6 bytes for Ethernet） |  | 
Target protocol address （For example，4 bytes for IP） |  | 
It is not filled in a request
Notes: 十

## Slide 14: Encapsulation of ARP packet
The byte order of ARP packet
Example：Ethernet frame
HType | PType | HL | PL | OP | sMAC | sIP | tMAC | tIP
2
2
2
1
1
6
6
4
4
ARP Packet
目的MAC
类型
FCS
源MAC
Packet
6
6
2
46 ~ 1500
4
byte
pad
28 bytes
46
0x0806
byte

## Slide 15: Example
A host with IP address 130.23.43.20 and physical address 0xB23455102210 has a packet to send to another host with IP address 130.23.43.25 and physical address 0xA46EF45983AB. The two hosts are on the same Ethernet network. Show the ARP request and reply packets encapsulated in Ethernet frames.

## Slide 16: Example: ARP Request

## Slide 17: Example: ARP Reply

## Slide 18: Example: ARP Request Packet

## Slide 19: Example: ARP Reply Packet

## Slide 20: 6.1.3 Proxy ARP
Hided
Q: In the same IP network or not?
“Honest”
Notes: 代理ARP

## Slide 21: Answer
RFC 925: Multi-LAN Address Resolution
  Explicit subnets
  Transparent subnets（Extended ARP）
Notes: 显式子网 透明子网 RFC925: The new element is the "magic box" ("ARP-based bridge") that relays the ARP request into neighboring LANs and acts as an agent for relaying datagrams to hosts on other LANs. The host must be able to decide if this IA is on this LAN or some other LAN. If on this LAN then use some procedure to find the HA. If on some other LAN then use some procedure to find the HA of a BOX.

## Slide 22: Answer
RFC 1027: Using ARP to Implement Transparent Subnet Gateways
  Routers: Explicit subnets
  Hosts: Transparent subnets
“ From the host point of view, there are no subnets, and their physical networks are simply one big IP network. ”
Notes: RFC-925 describes a general mechanism for dynamic subnet routing using Proxy ARP and routing caches in the gateways. Our technique is restricted subset of RFC-925, in which we use static subnet routes which are determined administratively. As a result, our transparent subnet gateways require no new network routing table entries nor ARP cache entries; the only tables which are affected are the ARP caches in the host

## Slide 23: RFC 1027 Discussion
.3向.35发送IP分组
  .3广播请求.35的ARP分组，R不转发广播
.35向.3发送IP分组
  .35广播请求.62的ARP分组
R
200.6.8.0/24
Main network
200.6.8.32/27
Hided network
.33
.34
.35
.62/27
.1/27
.3
.4
.5
 IP发送失败
 IP发送成功
 ARP失败
 ARP成功
Solution：
R代替.35向.3返回ARP应答
—— Proxy ARP
Notes: In our implementation, routing loops are prevented by proper administration of the subnet routing tables in the gateways.

## Slide 24: 6.1.4 Gratuitous ARP
Duplicate address test
A
B
202.115.12.34
202.115.12.34
1. ARP request: sIP = tIP = 202.115.12.34
2. ARP reply:
sIP = tIP = 202.115.12.34
3. Disable local interface: 202.115.12.34
Startup or
Change IP address
W. Stevens: 《TCP/IP Illustrated Volume 1: The Protocol》
Notes: 免费/无故的 ARP，可以有两个方面的作用：1) 一个主机可以通过它来确定另一个主机是否设置了相同的I P地址；2) 如果发送免费ARP的主机正好改变了硬件地址（很可能是主机关机了，并换了一块接口卡，然后重新启动），那么这个分组就可以使其他主机高速缓存中旧的硬件地址进行相应的更新。

## Slide 25: 6.2 ARP Package
Notes: 由5个部分构成

## Slide 26: 6.2 ARP Package
高速缓存表
Notes: 高速缓存表用于减少每一次数据报发送时的 ARP协议过程

## Slide 27: 6.2 ARP Package
队列
Notes: 未分配物理地址的分组

## Slide 28: 6.2 ARP Package
输入模块
Notes: 未分配物理地址的分组

## Slide 29: 6.2 ARP Package
输入模块
Notes: 未分配物理地址的分组

## Slide 30: 6.2 ARP Package
输出模块
Notes: 未分配物理地址的分组

## Slide 31: 6.2 ARP Package
输出模块
Notes: 未分配物理地址的分组

## Slide 32: 6.2 ARP Package
高速缓存表例子
Notes: 未分配物理地址的分组

## Slide 33: 6.2 ARP Package
高速缓存表例子
Notes: 未分配物理地址的分组

## Slide 34: 6.2 ARP Package
高速缓存表例子
Notes: 未分配物理地址的分组

## Slide 35: 6.2 ARP Package
高速缓存表例子
Notes: 未分配物理地址的分组

## Slide 36: ARP Cache
Host（Windows XP）
Router（Cisco）
C:\> arp –a
Interface: 202.115.12.34 --- 0x2
Internet Address Physical Address Type
202.115.12.33 00-90-27-a7-98-41 dynamic
202.115.12.47 00-90-27-1d-d9-94 dynamic
202.115.12.62 00-90-27-1a-67-e7 dynamic
Router# show arp
Protocol Address Age (min) Hardware Addr Type Interface
Internet 202.115.12.33 -- 0090.27a7.9841 ARPA Ethernet0
Internet 202.115.12.34 5 0005.5d06.1418 ARPA Ethernet0
Internet 202.115.13.1 -- 00e0.7bc0.b205 ARPA Ethernet1
Notes: 此处是ARP cache，前面是ARP软件包中的缓存表

## Slide 37: Discussion
更新ARP绑定时，发现已有的绑定与新的绑定不一样，是保持已有的还是替换它？
封装IP报文的以太帧中的源MAC和IP报文中的源IP可否用于刷新ARP表项？目的MAC和目的IP呢？
教材第3版第150页中ARP输入模块描述有误
  参见RFC 826中的Packet Reception一节
  关键问题：用什么地址查ARP缓存？什么情况下创建新的ARP表项？

## Slide 38: RFC References
RFC 1122: Requirements for Internet Hosts -- Communication Layers
  Section 2.3.2: ARP cache, ARP packet queue
RFC 1812: Requirements for IPv4 Routers
  Section 3.3.2
RFC 1433: Directed ARP
  ARP helper address
RFC 1868: ARP Extension – UNARP
  Announce leaving

## Slide 39: 6.3 RARP
Reverse Address Resolution Protocol
  RFC 903：MAC地址  IP地址
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access
Layer
Transport Layer
Application Layer

## Slide 40: RARP Operation
Purpose
  无盘机器的引导、动态IP地址配置
Packet format
  与ARP分组相同
  Operation：3 – RARP request，4 – RARP reply
Ethernet frame encapsulation
  类型：0x8035
Operation
  RARP request：广播发送，sIP、tIP不填，sMAC = tMAC
  RARP reply：仅由RARP服务器单播发送

## Slide 41: Alternative Solutions to RARP
RARP 只能获得IP地址
DHCP
BOOTP
掩码
默认网关
DNS 服务器

## Slide 42: 6.4 Summary
ARP
  作用、分组格式
  操作
    何时发送、送给谁
    发送方式（单播、广播）
    发送内容（ARP分组各字段的具体取值，以及封装该分组的以太帧中各字段的具体取值）
  Proxy ARP、Gratuitous ARP
RARP
  作用、操作、缺陷