## Slide 1: Chapter 11 Routing Protocols
Interior and exterior routing
Distance vector routing & RIP
Link state routing & OSPF
Path vector routing & BGP-4

## Slide 2: Introduction
Routing Table
  Static route  manually define
  Dynamic route  routing protocol
Table-driven routing
  One router  More routed protocols
  One routed protocol  One routing table
  One routed protocol  More routing protocols
Routing protocol
  To share the knowledge about the internet
  To calculate the routing table based on the topology or the policies
Convergence
Overhead
Scalability
Notes: 收敛，成本，可扩展

## Slide 3: Metric（度量）
Information used by a routing protocol to select the best path for routing
  The total metric of a route = the sum of the metrics of networks that comprise the route
  A router chooses the route with the shortest metric
Factors
  Hop count, bandwidth, delay, MTU, load, reliability, …
  Routing protocols can use one or more different factors to calculate a metric
A
D
C
B
Net
64K
64K
10M
10M
10M
Hop count: A  B  Net
Bandwidth: A  C  D  Net

## Slide 4: Convergence（收敛）
Convergence
  All routers in a network agree on the topology
Convergence time
  A measure of how quickly to recover from network changes
Factors affecting convergence
  The routing protocol used
  A router’s distance from the point of change
  The number of routers in the network
  Bandwidth and traffic load on communications links
  A router’s load
  Traffic patterns in relation to the topology change

## Slide 5: 11.1 Interior & Exterior Routing
Autonomous system（自治系统，AS）
  A group of networks and routers under the authority of a single administration
  Each AS typically represents an independent organization and applies its own unique routing and security policies
AS number
  An identifying number that is assigned by an Internet registry or a service provide
  Range: 1~65535
  Private AS number: 64512~65535

## Slide 6: IGP vs. EGP
IGP: Interior Gateway Protocol（内部网关协议）
  To be used within an autonomous system
  To find the best path to the network
  Example：RIP、OSPF、IS-IS
EGP: Exterior Gateway Protocol（外部网关协议）
  To be used between autonomous systems
  To find the best path to the AS
  Example：BGP-4
Note
  The static routing or an IGP could also be used between autonomous systems in some case
AS1
AS2
R
R
EGP
IGP
IGP

## Slide 7: Routing Protocols
Routing protocols
  Concept of the routing method
  Features and messages
  Operation
Protocol | Type | Routing method | Popular ver.
RIP | IGP | Distance vector routing | RIPv1, RIPv2
OSPF | IGP | Link state routing | OSPFv2
BGP | EGP | Path vector routing | BGP4

## Slide 8: 11.2 Distance Vector Routing
Initialization
  Directed routes: directed network & metric
Sharing the knowledge about the internet
  What the routing table – network & metric
  Where only with the immediate neighbors
  When periodical & triggered
Updating the routing table
提供了指向网络的路标 ！

## Slide 9: Updating
A
D
C
B
E
3
2
5
4
4
3
①
③
②

## Slide 10: Routing Loop: Two-node instability
Net 1
Net 2
Net 3
Net1 |  | 
…… | … | …
Routing table
Net1 |  | A
…… | … | …
Routing table
A
B
You can reach net1 through me with length 2
B can reach net1 ! Great !
Hop count changed !
-
1
16
2
3
Hop count changed !
4
-
B
∞
∞
B: ( net1, 2 )
A: ( net1, 3 )
B: ( net1, 4 )

## Slide 11: Some Remedies for Instability
Defining infinity（定义无穷大）
  Use a finite metric value to represent "infinity“
    The value must be large enough that no real metric would ever get that large
Triggered update（触发更新）
Split horizons（水平分割）
Poison reverse（毒性逆转）
  A variation of split horizons
None of them are 100% effective !

## Slide 12: Triggered Update
An attempt to speed up the convergence
  If there are no changes on the network
    To send update messages at usual 30-s intervals
  If there is a change
    To send update messages almost immediately
Special handling in RIP
  To limit the frequency of triggered updates
    Set a timer for a random time between 1 and 5 s
    A single update is triggered when the timer expires
  To limit the routes included in triggered updates
    At least those changed routes

## Slide 13: Split Horizons
Net 1
Net 2
Net 3
A
B
Net2 1
Net3 2
Net1 1
RIP messages
Net1 2
Net2 1
Net3 1
RIP messages
Notes: 分割范围，只交换 该端口之外的连接信息，如路由器A给B的信息只有Net1 1

## Slide 14: Poison Reverse
Net 1
Net 2
Net 3
A
B
Net2 1
Net3 2
RIP messages
Net1 16
Net2 16
Net3 16
Net1 1
RIP messages
Net2 16
Net3 1
Net1 16
Net2 1
Net3 16
Net1 2
Disadvantage:
Increasing the size of
the routing messages
Notes: 一直删除某端口的信息，会造成 该节点链路断开 与 分割范围机制的混淆，因此加入 Poison Reverse机制，将交换信息的本端口反向度量设置为无穷大(usually 16),”不要使用这个数值，因为我所知道的数值来源于你”

## Slide 15: More-node instability
1. Net 1 unreachable, then E sends a triggered
update to its neighbor A
2. Then A knows Net 1 is unreachable from E,
then sends a triggered update only to neighbors
B and D because of the split horizons
3. B and D know Net unreachable from A, then send a triggered update only to the neighbor C because of the split horizons
4. Assume that C has known about Net 1 from B, and C sends a regular update about Net 1 is accessible to D before the triggered update has been received.
5. Then D think Net 1 can be reachable through C, so D updates its routing table and informs A  routing loop
Net 1
A
B
C
D
E

## Slide 16: Hold-down Timer, 抑制定时器
To prevent update messages from reinstating inaccessible routes —— not in RFC
  When a router receives an update that indicates a network is unreachable, it starts a hold-down timer ( 180 s )
  While the hold-down timer is running, the router will NOT accept any update about the inaccessible route UNLESS
    the update comes from the originator of the previously inaccessible update
    or from a router reporting a better metric to the inaccessible network
Notes: 1.更新计时器（update）：30S更新路由表；2.无效计时器（invalid）：180S不刷新则将该路由条目的度量值设置为16；
3.刷新计时器（flush）：默认240S，比无效计时器长60S，刷新后路由条目则删除；4.抑制计时器（Hold-down）：180S。

## Slide 17: 11.3 RIP
Routing Information Protocol，RIP
  v1：RFC 1058，v2：RFC 2453，路由信息协议
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access Layer
TCP
UDP
Transport
Layer
RIP
Application
Layer
520
软件实现层次
RIP = RIPv1
Notes: RIP是一个应用层协议，基于UDP，端口号为520

## Slide 18: Example of a domain using RIP
Metric: hop count（跳数）
Infinity = 16, means unreachable
The maximum hop count = 15
Notes: Hops个数，也意味着delivery次数，无穷大被定义为16，则最大跳数不能超过15

## Slide 19: 11.3.1 RIP Message
Format ( <=512 bytes )
Encapsulation: UDP ( port 520 )
Command
Version
IP address
All 0s
All 0s
All 0s
Metric ( hop count )
All 0s
Family = 2
Repeated
Notes: 命令字段指明报文类型，请求(1)或响应(2)，RFC中原本还有3 4 已被废弃不用，5用于Sun Microsystems， 8bits版本号，目前有2个版本 V1和V2，本章讨论V1，family/系列，2为TCP/IP，14个字节的网络地址，目前只用到 IP address4字节，Metrics为hops，该表格称为1个表项entry

## Slide 20: Types of Messages
Request ( Command = 1 ): broadcast
  All entries ( IP address = 0.0.0.0 )
    To be sent by a router that has just come up
  Specific entries ( IP address ≠ 0.0.0.0 )
    To be sent by a router that has some time-out entries
Response ( Command = 2 )
  Solicited: unicast to the asker
    To be sent only in answer to a request
  Unsolicited: broadcast to every neighbor
    To be sent every 30 s, contain the entire routing table
Notes: 特定项目请求/所有项目请求， 询问的响应，非询问响应

## Slide 21: 11.3.2 RIP Operation
Discovery
Topology change
Calculating
  RIP updating algorithm
Initialize
RT
Send
RT
Update RT
Update?
Send RT per 30s
No
Yes
Find the change
Update
RT
Send RT
on schedule
Like discovery
Split horizons & poison reverse
Triggered update

## Slide 22: Initializing the Routing Table
Only the directly attached networks
  RFC 1058: metric = 1
  In most routers: metric = 0
Examples of some router’s routing table
  Cisco router
  C 10.1.1.0 is directly connected, FastEthernet0/0
  华为 router
  Dst/Mask Proto Pref Metric Nexthop Interface
  10.1.1.0/24 Direct 0 0 10.1.1.254 Ethernet0
……
……
RFC 1058: section 3.6
Notes: 本地局域网10.1.1.0 ，Pref 用于多路由协议中的优先级，值越小则优先级越高，0表示直接路由

## Slide 23: RFC 1058: Sending RIP Responses
Source IP address
  The IP address of the sending interface
  Consider: multiple IP addresses on a single physical interface
The entries
  Answer to a request: the requested routes
  Regular update: the whole routing table
  Triggered update: only the changed routes
  Note: the max datagram size is 512 bytes
In each entry
  Address: host addr, subnet addr, network addr, 0.0.0.0
  Metric: from the routing table without change
Notes: RFC 1058: section 3.4.2，“在路由设置两个虚拟接口192.168.0.1(/24)及192.168.1.1(/24)如果从192.168.0.0网络访问路由器该路由的主接口就是192.168.0.1,如果通过192.168.1.0网络访问该路由器,该路由器的主接口为192.168.1.1”

## Slide 24: RFC 1058: Updating the Routing Table
When receive a response RIP message
First to check for validity
  Port number, source IP address
Then to process the entries in it one by one
  1. Ignore the entry whose metric, address or unused fields are invalid
  2. Update the entry’s metric = min ( metric + 1, 16 )
  3. If the entry address is not in the RT, then add it
  4. Else if the next-hop in the RT is same with source IP address, then replace the route in the RT with this entry
  5. Else if the new metric is lower than the one in the RT, then replace the route in the RT with this entry

## Slide 25
RFC1058：
发送时 unchanged
接收时 Metric + 1
某些实现：
发送时 Metric + 1
接收时 unchanged

## Slide 26: Network Discovery
A
B
C
N1
N2
N3
N4
1
2
1
2
1
2
N3 | - | 1 | 0
N4 | - | 2 | 0
N1 | - | 1 | 0
N2 | - | 2 | 0
N2 | - | 1 | 0
N3 | - | 2 | 0
路由表：
目的网络 | 下一跳 | 发送接口 | Metric


N3
N1
N2
B1
2
1
A2
1
1
B2
1
1
C1
2
1
N4
A: (N1, 1) (N2, 1)
B: (N2, 1) (N3, 1)
C: (N3, 1) (N4, 1)
B: (N2, 1) (N3, 1)


N4
B1
2
2
N1
B2
1
2
A: (N1,1) (N2,1) (N3,2)
B: (N2,1) (N3,1)
(N1,2) (N4,2)
C: (N3,1) (N4,1) (N2,2)
B: (N2,1) (N3,1)
(N1,2) (N4,2)


A:(N1,1)(N2,1)(N3,2)(N4,3)
B: (N2,1) (N3,1)
(N1,2) (N4,2)
C:(N3,1)(N4,1)(N2,2)(N1,2)
B: (N2,1) (N3,1)
(N1,2) (N4,2)

## Slide 27: Topology Change
A
B
C
N1
N2
N3
N4
1
2
1
2
1
2
N3 | - | 1 | 0
N4 | - | 2 | 0
N1 | - | 1 | 0
N2 | - | 2 | 
N2 | - | 1 | 
N3 | - | 2 | 0


N3
N1
N2
B1
2
1
A2
1
1
B2
1
1
C1
2
1
N4

N4
B1
2
2
N1
B2
1
2
B: (N2,16) (N3,1)
(N1,16) (N4,2)
A: (N1,1) (N2,16)
(N3,16) (N4,16)
0
0
∞
∞
∞
C: (N3,1) (N4,1)
(N2,16) (N1,16)
∞
∞
∞
∞

## Slide 28: 11.3.3 Timers in RIP
Timers
Garbage collection
120 s
(for each route)
Expiration
180 s
(for each route)
Periodic
30 s
(for each router)
E = 180 s
E = 180 s
Metric 16
G = 120 s
25~35 s
180 s
删除
路由
120 s
实现中：
P＝25 ~ 30 s
G＝60 or 120 s
Notes: 1.更新计时器（update）：30S更新路由表；2.无效计时器（invalid）：180S不刷新则将该路由条目的度量值设置为16；
3.刷新计时器（flush）：默认240S，比无效计时器长60S，刷新后路由条目则删除；4.抑制计时器（Hold-down）：180S。

## Slide 29: 11.3.3 Timers in RIP

## Slide 30: 11.3.4 RIP Version 2
Message format
Operation
  Support VLSM and classless addressing: subnet mask
  Authentication: Family = 0xFFFF
  Multicasting: 224.0.0.9
  Encapsulation: UDP ( port 520 )
Command
Version
IP address
Subnet Mask
All 0s
Next Hop
Metric
Route Tag
Family
Notes: Family = 0xFFFF时，报文为专门的鉴别信息，16字节，同时Route tag字段被替换为鉴别类型 指明鉴别的协议
Multicasting 224.0.0.9 (all-router,全路由器)用来把报文传送给路由器，而不用包含主机

## Slide 31: Route Tag
路由标记
  To provide a method of separating "internal" RIP routes (routes for networks within the RIP routing domain) from "external" RIP routes, which may have been imported from an EGP or another IGP
N1
IR1
IR2
XR1
RIPv2
OSPF
N2, N3
Dest. | Next | Tag
N1 | IR1 | 1
N2 | IR3 | 2
N3 | IR3 | 2
IR3

## Slide 32: RFC2453 - Appendix A: Next Hop Field in a rip entry
Assume the best routes
  XR1  N1/N2; XR2  N3/N4/N5; XR3  N6/N7
XR1 exchange RIPv2 routes with IR1/IR2/IR3, setting the Next Hop field
  0.0.0.0 for N1/N2
  XR2 for N3/N4/N5
  XR3 for N6/N7
IR1
IR2
IR3
XR1
XR2
XR3
RIPv2
OSPF
Notes: Next hop指明下一跳必须发往的地址，无论是否在一个AS内

## Slide 33: 11.4 Link State Routing
Notes: 每个结点掌握全局信息，通过每个结点贡献自己的局部知识，来构建全局知识，就像共用一个地图，每个人的位置不同，走的路径也不一样

## Slide 34: 11.4 Link State Routing
Initialization
  States of directed links
Sharing the knowledge about the internet
  What the state of its neighborhood ( LSA )
  Where with every other router ( flooding )
  When there is a change ( event-driven )
Updating the routing table
  Dijkstra algorithm: SPF tree  Routing table
The idea —— 提供一张公路线路图！
Every router should have the whole “picture” of the internet
Notes: 拓扑必须是动态更新的，如何扩展到全局？四组动作:LSA, flooding, SPF tree  Routing table

## Slide 35: 11.4.1 Link and Link-State
Link
  A connection
Link-state
  The interface of a router and its relationship to its neighboring routers
  A directed graph（有向图）
    Vertices: routers and networks
    Edge: connect 2 router
    or connect a router to a network
Notes: 有向图，同一个链路两个方向的代价是不同的

## Slide 36
3
3
3
2
2
5
2
2
5
Metric: cost, 代价
The output side of each router interface
Ex. OSPF: 108 / bandwidth
Link state knowledge

## Slide 37: 11.4.2 Flooding
LSP —— IS-IS
  Link State Packet，链路状态分组
  IS-IS
LSA —— OSPF
  Link State Advertisement，链路状态通告
  A Link State Update ( LSU ) packet may contain several distinct LSAs
  To reliable floods each LSA one hop further from its point of origination

## Slide 38: 11.4.2 Flooding

## Slide 39: Reliable Flooding LSA
Each newly received LSA must be acknowledged
  Explicit: Link State Acknowledgment (LSAck) packets
  Implicit: LSU packets
  Many ACKs may be grouped together into a single LSAck packet
Determining which LSA is newer, then flooding the new (and more recent) LSA out some set of the router's interfaces
  LS sequence number  LS checksum LS age
  larger larger smaller
Retransmitting LSAs until they are acknowledged
  Retransmissions interval is a configurable per-interface value

## Slide 40: 11.4.3 Dijkstra Algorithm
Calculating a tree of shortest paths with the router itself as root
Divides the nodes into 2 sets
  Tentative（临时）
  if pass the criteria
  Permanent（永久）
Notes: 收到所有的LSP后，各个结点就会有一个完整拓扑的副本，但要找到到其它所有结点的最短路径，还需要使用最短路径树SPT

## Slide 41: 11.4.3 Dijkstra Algorithm

## Slide 42: 11.4.3 Dijkstra Algorithm

## Slide 43: SPF Algorithm Example
B
C
F
7
2
2
2
4
2
3
3
H
D
E
G
2
6
1
(2, A)
(4, B)
(8, B)
(5, B)
(6, B)
(7, B)
(9, B)
节点 | Cost | 路径 | E |  | 
B |  |  | F |  | 
C |  |  | G |  | 
D |  |  | H |  | 
2
∞
∞
∞
∞
∞
7
A-B
A-B-E
A-G
4
A-B-C
8
A-B-E-F
5
A-B-E-G
6
A-B-E-F-C
8
A-B-E-F-H
7
A-B-E-G-H
10
A
9
A-B-E-F-H-D
A-B-C-D
11
兰色表示路径{s}
Notes: 兰色表示路径{s}

## Slide 44: Build a Routing Table Based the SPF Tree
B
C
F
7
2
2
2
4
2
3
3
H
D
E
G
2
6
1
(2, A)
(4, B)
(8, B)
(5, B)
(6, B)
(7, B)
(9, B)
A
Node | Cost | Next | Node | Cost | Next
B | 2 | － | F | 5 | B
C | 8 | B | G | 6 | B
D | 9 | B | H | 7 | B
E | 4 | B |  |  | 

## Slide 45: 11.5 OSPF
Open Shortest Path First，OSPF
  v2：RFC 2328，开放最短路径优先
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access Layer
TCP
UDP
Transport
Layer
OSPF
Application
Layer
89
软件实现层次

## Slide 46: 11.5.1 Areas
Advantages
  Reduce link state advertisements overhead
  Reduce frequency of SPF calculations
  Smaller routing tables
Routing
  Intra-area routing
  Inter-area routing

## Slide 47: OSPF Area
A collection of networks, hosts, and routers all contained within an AS
Autonomous System
Area 1
Area 2
Area 0 (backbone)
To
other
ASs

## Slide 48: Area 0
Area 2
Area 3
Area 0
Area 1
Area 0
Backbone area
  Be responsible for distributing routing information between non-backbone areas
Must be contiguous
  NOT need be physically contiguous
  Virtual link
Area 0
Area 2
Area 1
Area 3

## Slide 49: OSPF Router Types
Internal router
Backbone router
Area Border Router, ABR
AS Border Router, ASBR
Autonomous System
Area 1
Area 2
Area 0 (backbone)
To other
AS
ABR，BR
IR
ASBR，BR
IR，BR

## Slide 50: 11.5.2 Network’s Type
Point-to-point network，点到点网络
Stub network，残桩网络
Transit network，转接网络
  Broadcast
  NBMA
Frame Relay
X.25

## Slide 51: Transit Network: DR and BDR
Designated router & backup DR —— a true router
  指定路由器 & 备份指定路由器
Purpose
  Reduce the number of adjacencies required on a broadcast or NBMA network
  Reduce the amount of routing protocol traffic and the size of the link-state database
Example: there are N routers on a transit network
  If no DR
    Each router has ( N-1 ) neighbors
  If there is a DR
    Each non-DR has only 1 neighbor
    DR has ( N-1 ) neighbors

## Slide 52: 11.5.3 OSPF LSA Types
Intra-area
  Type 1: Router–LSA
  Type 2: Network–LSA
Inter-area
  Type 3: Summary–LSA
  Type 4: Summary–LSA
External
  Type 5: AS–external–LSA

## Slide 53: Intra-area LSAs
Type 1: Router–LSA
  Originated by all routers
  Describes the collected states of the router’s interfaces to an area
  Flooded throughout a single area only
Type 2: Network–LSA
  Originated for broadcast and NBMA networks by the DR
  Contains the list of routers connected to the network
  Flooded throughout a single area only

## Slide 54: Inter-area LSAs
Type 3: Summary–LSA
  Originated by ABRs
  Describes routes to networks outside the area
  Flooded throughout the LSA’s associated area
Type 4: Summary–LSA
  Originated by ABRs
  Describes routes to ASBRs
  Flooded throughout the LSA’s associated area

## Slide 55: External LSAs
Type 5: AS–external–LSA
  Originated by ASBR
  Describes a route to a destination in another AS
  Flooded throughout the AS except the stub area

## Slide 56: OSPF LSA Example
Area 1
Area 0
Area 2
(Stub)
AS 10
AS 20
Type 2
(Area 1)
Type 3
(Area 1)
Type 5
(AS 20)
Type 3
Default
Type 1
(X=ASBR)
Type 3
(Area 1)
Type 5
(AS 20)
Type 1
(X=ASBR)
Type 3
(Area 1)
Type 1
(Area 1)
Type 1
(Area 0)
Type 3
(Area 0)
Type 5
(AS 20)
Type 4
(X=ASBR)
Type 1
(Area 0)
Type 5
(AS 20)
Type 4
(X=ASBR)
DR
Type 3
(Area 0)
Type 3
(Area 0)
Type 1
(Area 1)
Type 1
(Area 1)
Type 5
(AS 20)
Type 4
(X=ASBR)
Type 2
(Area 1)
Type 2
(Area 1)

## Slide 57: 11.5.4 OSPF Databases
Adjacency database
  All the neighbors to which a router has established bidirectional communication
  Unique for each router
Link-state database
  The relationship between each router and its neighbors
  All routers within an area have identical link-state databases
Forwarding database ( routing table )
  The routes generated when an SPF algorithm is run on the link-state database
  The routing table on each router is unique

## Slide 58: 11.5.5 OSPF Packets
Format
Multicasting: 224.0.0.5, 224.0.0.6
Encapsulation: IP ( protocol 89 )
Version
Type
Router ID
Area ID
Packet Length
Authentication
Authentication
Authentication Type
Checksum
Header
OSPF Packet Data

## Slide 59: Packet Types
1: Hello packet
  A 64-byte packet sent periodically to keep a link “alive”
2: DBD ( Database Description )
  Summary contents of a router’s link-state database sent to a newly discovered neighbor
3: LSR ( Link-State Request )
  Requests more specific information about a link from a neighbor’s link-state database
4: LSU ( Link-State Update, LSA )
  Transports LSAs to neighbor routers, a reply to an LSR
5: LSAck ( Link-State Acknowledgement )
  Ack receipt of a LSA; OSPF’s routing updates are connection-oriented

## Slide 60: LSU Packet Format
OSPF common header
24 bytes, Type = 4
Repeated
LSAs
(any combination of different kinds)
# LSAs ( 1 byte )

## Slide 61: LSA Format
Header
LSA data
LS sequence number
Advertising Router ID
Link state ID
LS checksum
length
LS age
Options
LS type

## Slide 62: Router ID
A 32-bit number assigned to each router running the OSPF protocol
  Uniquely identifies the router within an AS
  Implementation strategy: to use the largest or smallest IP interface address assigned to the router
Route ID —— in OSPF packet header
  The Router ID of the packet's source
Advertising Router ID —— in LSA header
  The Router ID of the router that originated the LSA

## Slide 63: Link State ID & Link ID
Link state ID —— in LSA header
Link ID —— in Router-LSA ( type 1 LSA )
LS type | Link State ID
1: router-LSA | The originating router's Router ID
2: network-LSA | The IP interface address of the network's DR
3: summary-LSA | The destination network's IP address
4: summary-LSA | The Router ID of the described ASBR
5: AS-external-LSA | The destination network's IP address
Link type | Link State ID
1: Point-to-point link | Neighbor Router ID
2: link to transit network | Interface address of DR
3: link to stub network | IP network address
4: virtual link | Neighbor Router ID

## Slide 64: 11.5.6 OSPF Operation
1. Establish router adjacencies
  Done with the exchange of Hellos
2. Elect the DR / BDR ( if necessary )
  Done on multiaccess network only
3. Discover routes
  Done in the ExStart and Exchange states
4. Select appropriate routes
  Done through the calculation of SPF algorithm
5. Maintain routing information
  Done through the regular exchange of Hellos

## Slide 65: OSPF States
Down: Not exchange information with any neighbor
Init: When an interface receives its first Hello
2-way: When it sees itself in a neighbor’s Hello
ExStart: Two neighbors use Hello to negotiate who is the “master” and who is the “slave”
Exchange: Neighbors use DBD to send each other a summary of their link-state database
Loading: Uses LSR, LSU, and LSAck to get complete link-state information
Full: Neighbors are fully adjacent

## Slide 66: Step 1. Establish router adjacencies
I am router ID 172.68.5.1 and I see no one
Down State
172.68.5.1/24
E0
172.68.5.2/24
E1
A
B
Router B 邻接表
172.68.5.1/24, int E1
Init State
I am router ID 172.68.5.2, and I see 172.68.5.1
Router A 邻接表
172.68.5.2/24, int E0
Two-way State
Hello
39547439070713
39547439070713
Hello
39547439070713
39547439070713

## Slide 67: Step 3. Discover routes
Hello Packet
A
B
Exstart
Exchange
Loading
Full
Hello Packet
DBD Packet
DBD Packet
LSAck Packet
LSAck Packet
LSR Packet
LSU Packet
LSAck Packet

## Slide 68: 11.5.7 RIP vs. OSPF
对网络拓扑的了解
路由计算方法
路由更新方式
路由更新内容
收敛速度
适用环境

## Slide 69: 11.6 Path Vector Routing
Path vector routing
  The AS boundary routers advertise the reachability of the networks in their own ASs to neighbor AS boundary routers
Policy routing
  Choose the best path for reaching the destination based on the value of path attributes

## Slide 70: Initial Routing Tables
AS 3
AS 1
AS 2
AS 4

## Slide 71: Stabilized Routing Tables
A1
B1
C1
D1
AS1
B2
B3
B4
A4
A2
A3
A5
C2
C3
D2
D3
D4
AS2
AS3
AS4
3
3

## Slide 72: Path Vector Routing Table
Path
  An ordered list of ASs that a packet should travel through to reach the destination
  Example
Loop prevention
Network | Next Router | Path
N01 | R01 | AS14, AS23, AS67
N02 | R05 | AS22, AS67, AS05, AS89
N03 | R06 | AS67, AS89, AS09, AS34
N04 | R12 | AS62, AS02, AS09

## Slide 73: 11.7 BGP-4
Border Gateway Protocol，BGP
  v4：RFC 1771，RFC 1772，边界网关协议
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access Layer
TCP
UDP
Transport
Layer
BGP-4
Application
Layer
179
软件实现层次

## Slide 74: 11.7.1 Types of AS
Single-homed AS
  Only one exit point to the outside
  Example: AS 1, AS 3
Multi-homed AS
  More than one exit point to the outside
  Example: AS 2
  Nontransit AS
    not allow transit traffic to pass through it
  Transit AS
    allow transit traffic to pass through it
AS 1
AS 2
R
R
R
AS 3
R

## Slide 75: When to and not to Use BGP
Figure A
  A single-homed AS does NOT usually need BGP, uses default route
Figure B
  Even if an AS has redundant paths to its ISP’s POP, BGP is NOT necessarily required
Figure C
  An AS with redundancy to the same ISP, but different POPs still does NOT require BGP
Figure D
  An AS with multiple ISPs REQUIRES BGP
Custom
AS
ISP
AS 1
A
Custom
AS
ISP
AS 1
B
Custom
AS
ISP
AS 1
ISP
AS 1
C
Custom
AS
ISP
AS 1
ISP
AS 2
D
BGP must be used to implement
external routing policies.

## Slide 76: 11.7.2 IBGP & EBGP Sessions
AS 1
R
AS 3
AS 2
R
R
R
R
AS 3
R
R
EBGP
EBGP
EBGP
EBGP
IBGP
IBGP
IBGP

## Slide 77: Synchronization Rule
Example
  A BGP router (A) can not advertise routes (15.1.1.0) learned from an IBGP peer (B) to other BGP peers unless the local router (C) also has learned about the route via an IGP
AS 200
17.1.1.0
A
B
AS 100
10.1.1.0
AS 300
15.1.1.0
IBGP
Non-BGP
Router
Router C has not learned about 15.1.1.0 via an IGP
C

## Slide 78: 11.7.3 BGP Path Attributes
Form: < type, length, value >
Types
  Well-known mandatory
    Example: ORIGIN (1), AS_PATH (2), NEXT_HOP (3)
  Well-known discretionary
    Example: LOCAL_PREF (5), ATOMIC_AGGREGATOR (6), AGGREGATOR (7)
  Optional transitive
  Optional non-transitive
    Example: MULTI_EXIT_DISC (4)

## Slide 79: NEXT_HOP Example

## Slide 80: LOAD_PREFERENCE Example
ANET will prefer LA to the network 128.213.0.0/16

## Slide 81: MED Example
RTA will prefer RTB to the network 180.10.0.0/16

## Slide 82: 11.7.4 BGP Messages
Message header
Encapsulation
  TCP ( port 179 )  unicasting
Type
Maker
（authentication or synchronization）
Length
16 bytes

## Slide 83: Message Types
Type 1: OPEN
  Establish the peer relationship
Type 2: UPDATE
  Advertise reachable or withdrawn routes using NLRI and path attributes
  NLRI: network layer reachability information
  < length, prefix >
Type 3: NOTIFICATION
  Inform the receiving router of errors
Type 4: KEEPALIVE
  Interval keeps peer relationship
  Recommend: 1/3 Hold Time interval

## Slide 84: 11.7.5 BGP Operation
Establish the BGP peer relationship
Exchange all candidate BGP routes, including withdraw routes
1.1.1.1
2.2.2.2
Net 6.0.0.0/8, 7.0.0.0/8
Net 4.0.0.0/8, 5.0.0.0/8
Net 4.0.0.0/8
Net 5.0.0.0/8
Net 6.0.0.0/8
Net 7.0.0.0/8
Net 6.0.0.0/8
Net 7.0.0.0/8
Net 4.0.0.0/8
Net 5.0.0.0/8
Withdraw 4.0.0.0/8

## Slide 85: BGP Routing Process Model
Input
Policy
Engine
Decision
Process
Routes
used by
router
Output
Policy
Engine
Routes
received
From
peers
Filtering
Attribute
manipulation
Choosing
the best
route
Routes
sent
to peers
BGP
Table
IP Routing
Table
Filtering
Attribute
manipulation

## Slide 86: 11.8 Summary
路由
  静态 vs. 动态
路由协议
  类型
    IGP：RIP、 OSPF
    EGP：BGP-4
  操作
    路由信息交换：what、 when、where
    路由计算